## Slide 1: The Von Neumann Architecture

## Slide 2
The Stored Program Computer Concept
1943: ENIAC
  Presper Eckert and John Mauchly -- first general electronic computer.
  Hard-wired program -- settings of dials, tubes and switches.
1944: Beginnings of EDVAC
  among other improvements, includes program stored in memory.
1945: John von Neumann
  wrote a report on the stored program concept, known as the First Draft of a Report on EDVAC
The basic structure proposed in the draft became known as the “von Neumann machine” (or model).
  a memory, containing instructions and data
  a processing unit, for performing arithmetic and logical operations
  a control unit, for interpreting instructions

## Slide 3
Basic Von Neumann Architecture

## Slide 4: Computer Memory
k x m array of stored bits (k is usually 2n)
Addresses (32bits, or 64bits)
  unique (n-bit) identifier of location
Contents
  m-bit value stored in location
Basic Operations:
LOAD
  read a value from a memory location
PROCESS
  process the data
STORE
  write a value to a memory location
•
•
•
0000
0001
0010
0011
0100
0101
0110
1101
1110
1111
00101101
10100010

## Slide 5: Interface to Memory
How does processing unit get data to/from memory?
MAR: Memory Address Register
MDR: Memory Data Register
To read a location (A):
  Write the address (A) into the MAR.
  Send a “read” signal to the memory.
  Read the data from memory to MDR.
To write a value (X) to a location (A):
  Write the data (X) to the MDR.
  Write the address (A) into the MAR.
  Send a “write” signal to the memory.

## Slide 6: Central Processing Unit
Functional Units
  ALU = Arithmetic and Logic Unit
  could have many functional units. some of them special-purpose (multiply, square root, …)
  ARM performs ADD, AND, NOT
Registers
  Small, temporary storage
  Operands and results of functional units
  ARM has several types of registers:
    Sixteen integer registers (R0, …, R15)
    Thirty two float registers (S0, …, S31)**
    Sixteen double registers (D0, …, D15)**
    Sixteen SIMD/Vector general purpose registers (Q0, …, Q15)**
    ** = will be covered towards the end of the course
Word Size
  number of bits normally processed by ALU in one instruction
  ARM registers can vary (R=32 bits, S=32 bits, D=64 bits, Q=128 bits)

## Slide 7: Control Unit
Orchestrates execution of the program
Instruction Register (IR) contains the current instruction.
Program Counter (PC) contains the address of the next instruction to be executed.
Control unit:
  reads an instruction from memory
    the instruction’s address is in the PC
  interprets the instruction, generating signals that tell the other components what to do
    an instruction may take many machine cycles to complete

## Slide 8: Instruction Processing
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory

## Slide 9: Instruction
The instruction is the fundamental unit of work.
Specifies two things:
  opcode: operation to be performed
  operands: data/locations to be used for operation
An instruction is encoded as a sequence of bits. (Just like data!)
  Often, but not always, instructions have a fixed length, such as 16, 32, or 64 bits depending on architecture.
  Control unit interprets instruction: generates sequence of control signals to carry out operation.
  Operation is either executed completely, or not at all.
A computer’s instructions and their formats is known as its Instruction Set Architecture (ISA).

## Slide 10: Example: ARM ADD Instruction
ARM has 32-bit long instructions.
  The structure of ADD is: ADD{cond}{flag} Rd, Rs1, Rs2
  Where:
    {cond} is an optional condition code (more on this soon!)
    {flag} is an optional flag code (more on this soon as well!)
    Rd is the destination register (where we store the result)
    Rs1 is the register containing first operand to add
    Rs2 is the second operand we are adding to Rs1.
  Example: ADD r6, r2, r3
    This adds the contents of register r2 to the contents of register r3, store result in r6
    In pseudocode this is: r6 = r2 + r3
ARM has about 80* registers (R0-R15, S0-S31, D0-D15, Q0-Q15) for temporary storage, and CPSR (*=varies based on version of ARM CPU).
  Sources and destination of ADD are registers.

## Slide 11: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Load contents of PC into MAR.
  Send “read” signal to memory.
  Read contents of MDR, store in IR.
Then increment PC, so that it points to the next instruction in sequence.
  On ARM chips, PC becomes PC+4 (other platforms may vary).
EA
OP
EX
S
F
D

## Slide 12: Instruction Processing: DECODE
First identify the opcode.
Depending on opcode, identify other operands from the remaining bits.
EA
OP
EX
S
F
D

## Slide 13: Instruction Processing: EVALUATE ADDRESS
For instructions that require memory access, compute address used for access.
Examples:
  add offset to base register (as in LDR)
  add offset to PC (or to part of PC)
  add offset to zero
EA
OP
EX
S
F
D

## Slide 14: Instruction Processing: FETCH OPERANDS
Obtain source operands needed to perform operation.
Examples:
  load data from memory (LDR)
  read data from register file (ADD)
EA
OP
EX
S
F
D

## Slide 15: Instruction Processing: EXECUTE
Perform the operation, using the source operands.
Examples:
  send operands to ALU and assert ADD signal
  do nothing (e.g., for loads and stores)
EA
OP
EX
S
F
D

## Slide 16: Instruction Processing: STORE
Write results to destination. (register or memory)
Examples:
  result of ADD is placed in destination register
  result of memory load is placed in destination register
  for store instruction, data is stored to memory
    write address to MAR, data to MDR
    assert WRITE signal to memory
EA
OP
EX
S
F
D

## Slide 17: Changing the Sequence of Instructions
In the FETCH phase, we incremented the Program Counter by 4*.
*= ARM, other platforms may vary.
What if we don’t want to always execute the instruction that follows this one?
  examples: loop, if-then, function call
Need special instructions that change the contents of the PC.
These are called jumps and branches.
  jumps are unconditional -- they always change the PC
  branches are conditional -- they change the PC only if some condition is true (e.g., the contents of a register is zero)

## Slide 18: Instruction Processing Summary
Instructions look just like data -- it’s all interpretation.
Three basic kinds of instructions:
  computational instructions (ADD, AND, …)
  data movement instructions (LD, ST, …)
  control instructions (branches)
Six basic phases of instruction processing:
F  D  EA  OP  EX  S
  not all phases are needed by every instruction
  phases may take variable number of machine cycles

## Slide 19: Driving Force: The Clock
The clock is a signal that keeps the control unit moving.
  At each clock “tick,” control unit moves to the next machine cycle -- may be next instruction or next phase of current instruction.
Clock generator circuit:
  Based on crystal oscillator
  Generates regular sequence of “0” and “1” logic levels
  Clock cycle (or machine cycle) -- rising edge to rising edge
“1”
“0”
time
Machine
Cycle